## Slide 1: MoonSane
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
Designing Lunar Habitats for Improving Mental Wellness
Notes: Welcome everyone, my name is Sophia and today I will tell you about my graduation project, called MoonSane. The objective is to design Lunar Habitats that are beneficial to the mental health of its inhabitants.

## Slide 2: Approaching Lunar Architecture
Extreme Environment
Blank Canvas
Notes: When approaching L A there are two sides to consider. On the one hand we have a blank canvas, providing new possibilities. On the other hand we are limited by the extremely hazardous environment.

## Slide 3: Habitat conditions
141:01:23 20871, 20890, and 20891 Source: NASA
Far away from home and family
Limited social circle
Habitat is main stimulus
3/67
Notes: Due to the dangerous surface conditions, astronauts will be mainly confined to the moonbase. This confinement can also cause psychological distress. Looking at logbooks of astronauts, the main concerns are of a social nature: being away from family and the small crew rotation.
They also mention the importance of the habitat interior. Any negative stimuli have a great impact, increasing the feeling of isolation.

## Slide 4: Views
AS17-136-20411-20425 Source: NASA
4/67
Notes: No comfort can be found in the surface view, it’s like a black and white photograph. An alien landscape. The apollo 11 crew also remarked that the horizon is closer, because the moon is smaller that Earth, adding to the claustrophobic feeling.

## Slide 5
AS17-138-21063 (OF300) Source: NASA
5/67
Notes: The only solace comes from the view of Earth in the sky, creating a connection to home and adding colour in beautiful shades of blue.

## Slide 6: Research question
How can human spatial perception be used in the design of Lunar habitats, to mitigate the negative mental health effects of living long-term on the moon?
6/67
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
Notes: My research question is

## Slide 7: Scope of habitat solutions
Lighting:
Allowing the passage of sunlight*
Habitat day/night cycles
Improved environmental lighting
Stimulating senses:
Improved colours of environment
Reduced noise levels
Variations in habitat environmental factors
Comfortable air temp/ humidity
Nature/plants included on station
Logan M. Smith, “The psychology and mental health of the spaceflight environment: A scoping review.” Acta Astronautica 201, 2022, 496-512, ISSN 0094-5765, https://doi.org/10.1016/j.actaastro.2022.09.054.
Crew interaction:
Private quarters
Views:
Views of the habitat from the windows
More observation windows
Direct views of earth
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
7/67
Notes: In a scoping review of suggested space habitat improvements, the solutions given in literature can be divided in four categories. Notable ones are ….

## Slide 8
Experiment: circadian rhythm lamps in the LUNARK module
  “Waking up to a sunrise inside our sleeping pods was an incredible natural feeling”
  Stationary
Light
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
https://www.saga.dk/projects/lunark/circadian
8/67
Notes: As a solution for the lighting this LUNARK project is a good example how to create a more varied lighting system. The participants found it very successful but this project is still stationary. It would be interesting to make it a dynamic system, with light direction changing like the sun moving across the sky for time-of-day orientation.

## Slide 9: Spatial enclosure
Enclosed spaces
  increase stress
  trigger avoidance
  Locomotive vs visual permeability
Enclosure is judged by visual permeability
Vartanian, O., Navarrete, G., Chatterjee, A., Fich, L. B., Gonzalez-Mora, J. L., Leder, H., ... & Skov, M. (2015). Architectural design and the brain: Effects of ceiling height and perceived enclosure on beauty judgments and approach-avoidance decisions. Journal of environmental psychology, 41, 10-18.
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
9/67
Notes: With respect to variations in visual stimuli I looked into characteristics of architectural spaces that affect the human psychological state. First is spatial enclosure. Research shows that more enclosed spaces increase stress. How enclosed a space is is judged by how much and how far a person can see through a space; this is called visual permeability.

## Slide 10: Spatial geometry
Study using VR
EEG, eye-tracking
Various rooms, different shapes
  Symmetric vs asymmetric
  Proportion
Asymmetric, angular spaces
  High pupil dilation- positive interest
  The more protrusion, the better
Shemesh, A., Leisman, G., Bar, M., & Grobman, Y. J. (2021). A neurocognitive study of the emotional impact of geometrical criteria of architectural space. Architectural Science Review, 64(4), 394–407. https://doi-org.tudelft.idm.oclc.org/10.1080/00038628.2021.1940827
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
10/67
Notes: I also investigated spatial geometry and how it impacts the viewer emotionally. This experiment using VR had subjects walk into differently shaped spaces and measured their reaction.
The results showed asymmetric spaces piqued the viewers interest, also the more protruding the shapes were, the more mentally engaged they were.

## Slide 11: Natural geometry: fractal patterns
Repeating shapes
  Calming effect
  Hidden in nature: biophilia
  Dynamic: light shimmer
Voronoi
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
Abboushi, B., Elzeyadi, I., Taylor, R., & Sereno, M. (2019). Fractals in architecture: The visual interest, preference, and mood response to projected fractal light patterns in interior spaces. Journal of Environmental Psychology, 61, 57-70.
11/67
Notes: Looking into geometry and psychology, I came across fractal patterns. The originate in nature. They are made up of the same shape repeating in decreasing scales. They provide a path for the brain to follow, inducing a form of hypnosis that calms down the mind and body. A notable pattern is called Voronoi, which has played a big role in this design.

## Slide 12: Natural geometry: Voronoi
Voronoi
  Point based pattern found in nature
  Scalable cells 2D or 3D
  Facetted geometry
Seamless fit
Adjustable density and size
Extra-terrestrial form language
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
12/67
Notes: Voronoi is a point based pattern that creates asymmetric facetted cells that fit together seamlessly. As this is a Extra-terrestrial design, it seemed important to find a new form language, different than on Earth and this seemed the right fit. It is flexible as it can be adjusted easily. It also seemed perfect for creating the asymmetric spatial geometry I have shown before.

## Slide 13: The Overview Effect
Phenomenon of astronauts who view Earth from space
Awe-inducing
  Increased empathy and sense of purpose
  Decrease in stress hormones
NASA
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
Nezami, A., Persaud, L. M., & White, F. (2021). The overview effect and well-being. In Expanding worldviews: astrobiology, Big history and cosmic perspectives (pp. 163-197). Cham: Springer International Publishing.
13/67
Notes: Adding more viewports to a habitat is preferred by astronauts because it reduces feelings of confinement. Permeability, remember? The earth view is most important because it facilitates a phenomenon called the Overview effect. When astronauts view earth from space it causes an intense emotional reaction that inhibits the fight-or-flight system.

## Slide 14: Earth gazing & “Skyspace”
James Turrell – “Skyspace”
looking upwards – positive effect
Earth view incorporated?
Mood lighting added to increase experience (based on mood of astronaut?)
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
14/67
Notes: It reminded me of an art installation I visited last year, called skyspace. It is a room with a skylight where you sit in silence looking at the sky, while the mood light changes around you. I would like to introduce such a reflection space to a habitat and combine it with the view of Earth, instead of the sky.

## Slide 15: Colour projection
“EMO”- Xiying Bao
AI technology: facial recognition
Changes colours and shapes based on perceived emotion
Adaptive system monitors wellbeing of crew members
  influence/transform emotions as well?
15/67
https://studentawards.mediaarchitecture.org/mab/project/11
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
https://designawards.core77.com/Interaction/104584/Emo.html
Notes: Such a space would be even more powerful if the colours change according to the mood of the astronaut, just like this project meant to visualise emotions after the mental strain of the pandemic. Using facial recognition software, the visitor’s emotion is identified and visualised. I would like to take it a step further, with the visuals being used to transform the feeling of the astronaut for the better.

## Slide 16: Concept
Designing a Lunar habitat that promotes mental wellness of the crew
Concept
Sophia Benfield | MoonSane | Lunar Architecture | Tutors: H. Bier & A. Hidding & F. Adema | 2024/25 | TU Delft
16/67
Notes: To summarise, I propose to design a Lunar habitat that improves mental wellness by combining a dynamic lighting system with spatial geometry and both inside as outside views. I also propose to add a meditation space combining the overview effect with mood lighting, where crew members can find peace of mind.