## Slide 1: Final Presentation
Simone Guccione - 6171796
Twan Linger - 4869656
Lorenzo Marzolini - 6190561
Manuel Oberhofer - 6564542
Alessandro Vercalli – 6288979
Pieter van der Werf - 5526353
TU Delft Space & Robotic Institutes
JIP 2025 Group 1.13.1
Back to the Moon
7/11/2025
Notes: Fin on top is emissivity heat exchanger (sending extra heat by the Laser to the walls of the tube 2,6 m^2)

## Slide 2: Problem Statement
Return humans
to the moon
Scientific research
WHY?
Notes: Space agencies and governments want to return humans back to the moon
Shipments to the moon are expensive --> Additives no feasible option
Scientific purpose --> not for bussiness
Infeasible to rely on human labor
Other possibilities if asked are :” Mining, solar farms, Possibility of moving more polluting industries from earth, Refueling post for mars missions and tourism.
Maybe communicate that commercial crewed lunar missions are simply not economically viable yet, and that this venture would not be intended as a commercial service for businesses but instead as a part of a space exploration program such as the Artemis program

## Slide 3: Problem Statement
Return humans
to the moon
Scientific research
Permanent settlement
Protective habitat
WHY?
WHAT?
Notes: Space agencies and governments want to return humans back to the moon
Scientific purpose --> not for business
Why protective habitat  next slide

## Slide 4: Hazards
Temperature (100 – 375) [K]
Chen, M. et al. (2018). AIAA SPACE Forum, Orlando, FL. DOI: 10.2514/6.2018-5109
Notes: -170 / +100 celsius across lunar day ( 14 days of light and 14 of darkness) (29.5 earth day == 1 moon day)

## Slide 5: Hazards
Temperature
Radiation (ISS: 190 | Moon: 500 ) [mSv/year]
Image credits: ESA
Astronaut career limit: 600 mSv
Notes: 0.1 mSv = 100 μSv = chest x-ray
Full body CT = 10 mSv
Limits: 600 mSv/career
190mSv/yr ISS
500mSv/yr moon
50 mSv career limit for regular earth worker

## Slide 6: Hazards
Temperature
Radiation
Micrometeorites (15 – 18) [km/s]
Image credits:
SatMagazine (top), ESA (bottom)
Notes: Top image: Electron micrograph image of an orbital debris hole made in the panel of the Solar Max satellite
This image shows the results of a lab test impact between a small sphere of aluminium travelling at approximately 6.8 kilometres per second and a block of aluminium 8 centimetres thick. This test simulates what can happen when a small space debris object hits a spacecraft.
Velocities up to 20 Km/s.
Size varies but it’s in the ballpark of a speckle of dust.

## Slide 7: Hazards
Temperature
Radiation
Micrometeorites
Moonquakes (up to 5) [mb]
Image credits to:
NASA/GSFC/Arizona State University
Notes: Maximum magnitude 5, usually 3.

## Slide 8: Lava Tubes
Image credits: NASA
Notes: Researcher have already found that a big part of the solution is to built the habitat inside a lava tube. Here it is already shielded partly against radiation and micro-meteorites. The lava tube also provides a more stable temperature of around –20 degrees.
Lunar lava-tubes have only being analyzed using pictures taken from the sky at different angles, the morphology of the inside space it’s still not certain to this day.
Experiment on Using LiDAR and Robotics to map lava-tunnel has being done on earth.

## Slide 9
Lava Tubes
Masayuki Naito et al 2020 J. Radiol. Prot. 40 947
Radiation
Notes: Lava tube naturally protects form meteorites impacts, radiation levels substantially lower.
Image: Spatial distribution of the effective dose equivalent at the vertical hole due to GCR protons during the solar minimum phase.
Image generated trough simulation.

## Slide 10
Lava Tubes
Radiation
Thermal environment
Ding, J. et al. (2022). Space: Science & Technology. DOI: 10.34133/2022/9875780
Notes: Simulation of the inside temperature of a lava tube, shadowed/illuminated area of the tube

## Slide 11: HOW?
In-situ resource utilization
High logistical costs (1000 $/gram)
Notes: Shipments to the moon are expensive --> Additives no feasible option
Infeasible to rely on human labor

## Slide 12: HOW?
In-situ resource utilization
Using manual labor infeasible
Autonomous robotic construction
High logistical costs (1000 $/gram)
Notes: Shipments to the moon are expensive --> Additives no feasible option 1000€/Kg
Infeasible to rely on human labor: need shielding while building

## Slide 13
By combining swarm robotics and additive manufacturing of lunar regolith we aim to autonomously construct a protective habitat inside a lava tube to facilitate permanent human presence on the moon.

## Slide 14
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Additive Manufacturing techniques
Notes: Three possible AM solution were considered

## Slide 15
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Terrestrial resources | 100% ISRU | 100% ISRU
Additive Manufacturing techniques
Notes: Bider-based needs a solid percentage of the 306 t of material to be shipped from earth, or in alternative heavy machinery to produce the binders on site (still uncertain process but it is being investigated by someone)

## Slide 16
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Terrestrial resources | 100% ISRU | 100% ISRU
Continuous operation | Discrete operation | Discrete operation
Additive Manufacturing techniques
Notes: Binder-based by design needs to be continuous due to the solidifying of the materials in the pipes and blockage

## Slide 17
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Terrestrial resources | 100% ISRU | 100% ISRU
Continuous operation | Discrete operation | Discrete operation
- | Melted > 1500 °C; not porous | Very porous
Additive Manufacturing techniques
Notes: SLM material is naturally porous if produced in a vacuum , the problem can be solved by either melting up to 1500 or melting twice as the Laser hannover guy said.

## Slide 18
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Terrestrial resources | 100% ISRU | 100% ISRU
Continuous operation | Discrete operation | Discrete operation
- | Melted > 1500 °C; not porous | Very porous
- | Compressive strenght > 90 [MPa] | ~ 60 [MPa]
Additive Manufacturing techniques
Notes: As the ESA guy said, you can get better properties with melting.
90 Mpa is better then most concrete making it a good material for construction.

## Slide 19
Binder-based​ methods | Selective Laser Melting | Selective Laser Sintering
Terrestrial resources | 100% ISRU | 100% ISRU
Continuous operation | Discrete operation | Discrete operation
- | Melted > 1500 °C; not porous | Very porous
- | Compressive strenght > 90 [MPa] | ~ 60 [MPa]
- | High energy; 1,5 kW | -
Additive Manufacturing techniques
Notes: Higher energy use then sistering.

## Slide 20: General Requirements
Compressive structure
Guo, Z.-S., Li, M., Xing, D., Liang, C.-G., Hao, B., & Ma, P.-C. (2025). Melting and solidifying behavior of lunar regolith simulant under a vacuum environment. Journal of the American Ceramic Society, 108(8), e20566. DOI: 10.1111/jace.20566
Notes: Compressive structure --> lunar regolith = good in compression, bad in tension

## Slide 21: General Requirements
Compressive structure
Allow for robot traversal
Analytical Configuration of Wheeled Robotic Locomotion. Retrieved from: https://www.researchgate.net/publication/2378232_Analytical_Configuration_of_Wheeled_Robotic_Locomotion
Notes: Compressive structure --> lunar regolith = good in compression, bad in tension
Allow for robot traversal: Shallow walls OR ramp/stairs
Narrow ramps create a potential bottleneck for the process

## Slide 22: General Requirements
Compressive structure
Allow for robot traversal
Sufficient living space
40 m3 per astronaut
2,3 m height (2/3 total area)
Image credits: Smitt / Getty Images
Notes: Compressive structure --> lunar regolith = good in compression, bad in tension
Allow for robot traversal: Ramps or shallow walls
Sufficient living space: 24 to 70 m^3 per astronaut, 40 is already optimal for the mission

## Slide 23: General Requirements
Compressive structure
Allow for robot traversal
Sufficient living space
Shield from radiations
Meurisse, A., Cazzaniga, C., Frost, C., Barnes, A., Makaya, A., & Sperl, M. (2020). Neutron radiation shielding with sintered lunar regolith. Radiation Measurements, 132, 106247. https://doi.org/10.1016/j.radmeas.2020.106247
Notes: Compressive structure --> lunar regolith = good in compression, bad in tension
Allow for robot traversal: Ramps or shallow walls
Sufficient living space: 24 to 70 m^3 per astronaut, 40 is already optimal for the mission

## Slide 24: Radiation Protection
Structure 50 m in
lava tube
Radiation reduced
by 40x
Notes: Assuming linearity factor of radiation reduction is always 40.
10 mSv/y is pretty strict actually

## Slide 25: Radiation Protection
Structure 50 m in
lava tube
10 mSv/year
Radiation reduced
by 40x
Walls: 26 cm
Notes: Assuming linearity factor of radiation reduction is always 40.
10 mSv/y is pretty strict actually

## Slide 26: Radiation Protection
Structure 50 m in
lava tube
10 mSv/year
Safety factor: 2x
Radiation reduced
by 40x
Walls: 26 cm
Walls: 54 cm
Notes: Assuming linearity factor of radiation reduction is always 40.
10 mSv/y is pretty strict actually

## Slide 27: Concepts
Concept 1
Prefabricated
Blocks
Notes: 2 Feasible concepts:
  Concept 1: Prefabricating blocks in controlled environment and interlocking this into the final structure
  Concept 2: Printing the final structure in place
In both cases:
Maximizing the use of local resources to reduce the logistical costs
Both concepts leverage the use of SLS to allow construction without bringing additives/binders
Membrane first inflated primairly since it is easier, compared to moving in some airtight internal structure after construction
secondarily to support the structure a bit during construction
Speak about the airlock

## Slide 28: Concepts
Concept 1
Prefabricated
Blocks
Concept 2
In-Situ Melting
Notes: 2 Feasible concepts:
  Concept 1: Prefabricating blocks in controlled environment and interlocking this into the final structure
  Concept 2: Printing the final structure in place
In both cases:
Maximizing the use of local resources to reduce the logistical costs
Both concepts leverage the use of SLS to allow construction without bringing additives/binders
Membrane first inflated primairly since it is easier, compared to moving in some airtight internal structure after construction
secondarily to support the structure a bit during construction
Speak about the airlock

## Slide 29: Concept 1: Prefabricated Blocks
Notes: Manufacturing of blocks on the surface, the printing machine can be inside the landers--> more controlled environment and we don't have to move them since are quite heavy (The earth one can reach 2000kg)
Transport of blocks to the construction site

## Slide 30: Concept 2: In-Situ Melting
Notes: Regolith is collected outside the lava tube
Transported into the lava tube where it is then processed

## Slide 31: Concept 2: In-Situ Melting
Notes: Two ways of in situ Melting depending on the thickness of each layer:
Thin layers(≈ 200 µm):
  Simultaneous depositing and sintering
  Laser(≈ 50W) on the robot
Thick layer(≈ 1 cm)
  Depositing at once and then sintering
  Fixed laser(≈5kW) reflected with mirrors

## Slide 32: Concept 2: In-Situ Melting
Melted regolith
Loose regolith
Newly deposited layer
Notes: Two ways of in situ sintering depending on the thickness of each layer:
Thin layers(≈ 200 µm):
  Simultaneous depositing and sintering
  Laser(≈ 50W) on the robot
Thick layer(≈ 1 cm)
  Depositing at once and then sintering
  Fixed laser(≈5kW) reflected with mirrors
Total construction time will be heavily dependent on the sintering speed of the laser and the total infill of the Voronoi pattern (now assuming 15%)

## Slide 33: Concept Selection
 | Concept 1 | Concept 2
Technical complexity |  | X
Technological maturity & risk |  | 
Adaptability |  | ✓
Reliability & maintenance |  | X
Structural integrity & durability |  | X
Construction time |  | X
Logistical cost |  | X
Notes: So to conclude: according to our argumentation concept 2 outperforms concept 1 on basically all of the 7 criteria except the technical maturity of the sintering techniques and and additional risks.
Full-scale in-situ laser sintering has never been attempted; while sintering components in a stationary SLS machine is already a recognized industrial process.

## Slide 34: Habitat Shape
3,8 m
20 m

## Slide 35: Habitat Shape
Works in compression
Req 1
3,8 m
20 m

## Slide 36: Habitat Shape
Maximum slope = 35°
Req 2
Works in compression
Req 1
3,8 m
20 m

## Slide 37: Habitat Shape
Maximum slope = 35°
Req 2
Works in compression
Req 1
Req 3
Internal habitable
Volume = 120 m3
3,8 m
20 m

## Slide 38: Habitat Shape
Maximum slope = 35°
Req 2
Works in compression
Req 1
Req 3
Internal habitable
Volume = 120 m3
Minimum wall
Thickness = 54 cm
Req 4
3,8 m
20 m

## Slide 39: System Overview

## Slide 40: System Overview
Notes: In the HUB communication with earth is done (1300 ms average latecy) and most of the Math for task planning and robot coordination is done.

## Slide 41: System Overview
Notes: Power is made on the surface and cables bring it to the various stations.

## Slide 42: System Overview
Notes: Repeaters are there to bounce the robot signal between the robots and the HUB.

## Slide 43: System Overview
Notes: Collector Robots are 8 and with the assumed distance they are the faster component of the process, needing just around half a year (of continuous op) to collect all material with the tightest availability of 0,8 given the rough working conditions.

## Slide 44: System Overview

## Slide 45: Robot Types & Systems
Number | 12 [-]
Weight | 30 [kg]
Speed | 0,3 [m/s]
Capacity | 30 [kg]
Energy | Battery
Collector – depositor – waste management
Image credits: NASA
Notes: Charging: 68 min 90 min/charge
PCM heat-sink; Thermal reset: 121 min
Collection rate: 0.15 kg/s
Counter rotating drums

## Slide 46: Robot Types & Systems
Processing machine
Dreyer, C. B., Walton, O., & Riedel, E. P. (2012). Centrifugal Sieve for Size-Segregation and Beneficiation of Regolith. Earth and Space 2012, ASCE. DOI: 10.1061/9780784412190.004
Number | 2 [-]
Output | 150 [kg]
Input buffer | 750 [kg]
Output buffer | 750 [kg]
Energy | Plugged-in
Notes: Sieve incoming regolith and split fine (0–2 mm) vs coarse (waste)
Expected total processed regolith: ~363 t

## Slide 47: Robot Types & Systems
Flattening Robot
Lee, R., Younes, B., Pletta, A., Harrington, J., Wong, R. Q., & Whittaker, W. R. (2023). CraterGrader: Autonomous robotic terrain manipulation for lunar site preparation and earthmoving. arXiv, abs/2311.01697. URL: https://api.semanticscholar.org/CorpusID:265019081
Number | 5 [-]
Weight | 25 [kg]
Capacity | 50 [m²/h]
Energy | Battery
Notes: Charging: 45 min 180 min/charge
250 mmgrading blade; Chain-mail drag mat
300 Wh battery

## Slide 48: Robot Types & Systems
Melting Robot
Image credits: GITAI
Number | 5 [-]
Weight | 330 [kg]
Printing speed | 1,725 [L/h]
Energy | Plugged-in
Notes: The robot is originally designed to assemble structures, and the arms are interchangeable.
Robot 280 Kg, dimensions (1800 x 1492 x 942,5 mm )(LxWxH)
Robotic arm 50 Kg and has a total length of around 2 m
High emissivity panels 2,6 m2 ops temperature 77 °C

## Slide 49: Robot Types & Systems
Charging Station
Image credits: Astrobotic
Number | 8 [-]
Weight | 2,9 [kg]
Capacity | 400 [W]
Energy | Plugged-in
Notes: 85% efficiency (really good, wireless phone chargers are usually 66%)
Number 8 chosen using Queueing theory with a 2,82 min expected waiting time
All wireless robots use this charging infrastructure

## Slide 50: Construction Process
Preparation mission
Notes: Surveying and setting up the necessary infrastructure using the GITAI robots

## Slide 51: Construction Process
Preparation mission
Construction mission

## Slide 52: Preparation Mission

## Slide 53: Power setup
Step 1: Solar panels
Notes: Mounting the solar panels and charging stations in a easy task for the GITAI rovers operating on battery

## Slide 54: Power setup
Step 2: Power distribution system

## Slide 55: Power setup
Step 3: Testing
Notes: Testing automatically the system

## Slide 56: Site preparation
Step 4: Surveying and assessing site
Notes: Find a flat spot and clear debris and rocks

## Slide 57: Site preparation
Step 5: Clearing the site

## Slide 58: Site preparation
Step 6: Scanning the site

## Slide 59: Construction mission

## Slide 60: Installation membrane​
Step 7: Transporting membrane & airlock
Notes: Towing from the ship the airlocks in place, membrane is already attached to the airlocks and ready to be deployed.

## Slide 61: Installation membrane​
Step 8: Deploying inflatable membrane

## Slide 62: Collection & processing
Step 9: Collecting regolith

## Slide 63: Collection & processing
Step 10: Transporting regolith

## Slide 64: Collection & processing
Step 11: Processing regolith

## Slide 65: Habitat construction
Step 12: Depositing layer of regolith
Notes: Each layer is deposited of the correct mass ammount on the structure and then flattened

## Slide 66: Habitat construction
Step 13: Flattening the layer of regolith

## Slide 67: Habitat construction
Step 14: Melting the fresh regolith

## Slide 68: Post construction
Step 15: Robot maintenance & cleaning

## Slide 69: Post construction
Step 16: Final inspection completed structure

## Slide 70: Regolith Melting Process
Silicon & oxides
Thermophysical properties
Notes: required -> 1.5 kW of power -> 3 kW laser (50% efficiency)
Regolith rich in silicon andoxides
Required laser powercalculated based onthermophysical properties
Temperature target of 1500 C

## Slide 71: Regolith Melting Process
Silicon & oxides
Thermophysical properties
Target temp: 1500 °C
Target speed: 1,725 L/h
Power needed: 1,5kW
Notes: required -> 1.5 kW of power -> 3 kW laser (50% efficiency)
Regolith rich in silicon andoxides
Required laser powercalculated based onthermophysical properties
Temperature target of 1500 C

## Slide 72
Power generation
Solar energy
Fuel cells
RTG's
Nuclear fission
Notes: Total power requirement of ~30 kW
Lasers are around half the power req

## Slide 73
Power generation
Solar energy
Fuel cells
RTG's
Nuclear fission
Notes: Total power requirement of ~30 kW
Fuel cells still new tech
RTG need a specific material that is produced very little a year making it very hard and long to acquire for a mission.
Nuclear fission is really practical idea but regulations prohibit to launch fission material into space.

## Slide 74: Power managing scenarios
Continuous operation

## Slide 75: Power managing scenarios
Continuous operation
68 tons of batteries
280 days to completion

## Slide 76: Power managing scenarios
Continuous operation
2. Day-time only operation
68 tons of batteries
280 days to completion

## Slide 77: Power managing scenarios
Continuous operation
2. Day-time only operation
68 tons of batteries
280 days to completion
1,1 tons of batteries
560 days to completion

## Slide 78: Cost Comparison
Category | Cost [€] | Cost [€]
Robotics | 22.100.000 | 22.100.000
Equipment | 160.015.500 | 140.745.939
Shipment | 74.043.000.000 | 5.238.129.360
Operational | 1.900.000.000 | 1.900.000.000
Total | 76.125.115.500 | 7.300.975.299

## Slide 79: Cost Comparison
Category | Cost [€] | Cost [€]
Robotics | 22.100.000 | 22.100.000
Equipment | 160.015.500 | 140.745.939
Shipment | 74.043.000.000 | 5.238.129.360
Operational | 1.900.000.000 | 1.900.000.000
Total | 76.125.115.500 | 7.300.975.299

## Slide 80: Cost Comparison
Category | Cost [€] | Cost [€]
Robotics | 22.100.000 | 22.100.000
Equipment | 160.015.500 | 140.745.939
Shipment | 74.043.000.000 | 5.238.129.360
Operational | 1.900.000.000 | 1.900.000.000
Total | 76.125.115.500 | 7.300.975.299

## Slide 81: Construction Time: Simulation set-up

## Slide 82: Construction Time: Simulation set-up

## Slide 83: Construction Time: Simulation set-up

## Slide 84: Construction Time: Results
Total construction time: 536 Earth days (268 of work)

## Slide 85: Construction Time: Results
Total construction time: 536 Earth days (268 of work)
Notes: Flattening robots are the faster at they work, Deposition gets a big improvement going from 2 to 3 robots, while malting takes the majority of the time

## Slide 86: Construction Time: Results
ROBOT TYPE |  | 
Activity | [h] | [%]
Working |  | 
Taveling |  | 
Charging |  | 
Cooling |  | 
Waiting Charge |  | 
Waiting process |  | 
Waiting input |  | 
Maintenance |  | 
Waiting Structure |  | 
Job finished |  | 

## Slide 87: Construction Time: Results
COLLECTORS |  | 
Activity | [h] | [%]
Working | 126 | 2
Traveling | 981 | 15,3
Charging | 857 | 13,3
Cooling | 668 | 10,4
Waiting Charge | 4 | 0,1
Waiting process | - | -
Waiting input | 2669 | 41,5
Maintenance | 1097 | 17,1
Waiting Structure | - | -
Job finished | 27 | 0,4
Notes: Since the collection is fast, with a finite buffer, robots spend a lot of time waiting to unload in front of the machine

## Slide 88: Construction Time: Results
DEPOSITORS |  | 
Activity | [h] | [%]
Working | 309 | 4,8
Traveling | 310 | 4,8
Charging | 523 | 8,1
Cooling | 407 | 6,3
Waiting Charge | 2 | 0,0
Waiting process | 7 | 0,1
Waiting input | - | -
Maintenance | 218 | 3,4
Waiting Structure | 4657 | 72,4
Job finished | 0,18 | 0,0
Notes: With three depositors 70%+ of the time is waiting

## Slide 89: Construction Time: Results
FLATTENERS |  | 
Activity | [h] | [%]
Working | 186 | 2,9
Traveling | 9 | 0,1
Charging | 26 | 0,4
Cooling | - | -
Waiting Charge | 0,52 | 0,52
Waiting process | - | -
Waiting input | - | -
Maintenance | 207 | 3,2
Waiting Structure | 6006 | 93,4
Job finished | 0,17 | 0,0
Notes: Flatteners spend most of their time waiting.

## Slide 90: Construction Time: Results
MELTERS |  | 
Activity | [h] | [%]
Working | 4138 | 64,3
Traveling | - | -
Charging | - | -
Cooling | - | -
Waiting Charge | - | -
Waiting process | - | -
Waiting input | - | -
Maintenance | 244 | 3,8
Waiting Structure | 2050 | 32
Job finished | - | -
Notes: Melters are the busiest robots

## Slide 91: Risk Management – Process
Framework: NASA CRM
Identification
Safety
Technical
Cost
Schedule
Notes: The risk management framework used in this project is largely based on the Continuous Risk Management Framework developed by NASA, but it has been adapted a bit to be more in line with the scope of this project.
First risks are identified and categorized as either a safety, technical, cost or schedule risk

## Slide 92: Risk Management – Process
Framework: NASA CRM
Identification
Analysis
Likelihood & severity rating (1-5)
Notes: The second step is risk analysis.
This starts by giving each risk two ratings; based on the risk’s severity and likelihood of it to occur

## Slide 93: Risk Management – Process
Framework: NASA CRM
Identification
Analysis
Likelihood & severity rating (1-5)
Risk score
Safety
Technical
Cost
Schedule
|2
|1,7
|1,4
|1
Notes: By multiplying the likelihood and severity rating, the risk score is obtained, which gives a measure of the actual risk level.
This risk score is then multiplied by a factor that based on its category, since certain risk categories have inherently greater potential to compromise mission success or safety.

## Slide 94: Risk Management – Process
Accept
Mitigate
Watch
Research
Framework: NASA CRM
Identification
Analysis
Response
Notes: Finally, a risk response is recommended, which are:
Accept: if the risk is low enough
Mitigate: Performing actions to reduce the risk
Watch:
Research: If the uncertainty about the underlying risk driver is large enough and more research is required to understand it

## Slide 95: Risk Management - Results
Technical
Majority of risks
Notes: The majority of the risks identified were technical risks

## Slide 96: Risk Management - Results
Technical
Majority of risks
Uncertainty about performance in lunar environment
Notes: Most of these risks centered around the performance of the systems in the lunar environment, since there are still a lot of uncertainties about it.
One big factor of uncertainty is also the degradation of the performance of systems over the 2 year duration of the mission

## Slide 97: Risk Management - Results
Technical
Majority of risks
Uncertainty about performance in lunar environment
Majority can be mitigated
Notes: Fortunately, we believe that the majority of these risks can be mitigated by either increasing redundancy in the system, or by including margins.
Some of these risks could also be mitigated by slightly altering some operational procedures

## Slide 98: Risk Management - Results
Technical
Safety
Biggest risks
Notes: The biggest risks to the project are safety risks

## Slide 99: Risk Management - Results
Technical
Safety
Biggest risks
Damage to (sub)structure
Notes: Most of these risks center about the inflatable substructure or the outer shell getting damaged.
The biggest risk is the possibility of the structure to get damaged by moon quakes
Other risks for damage include collisions between robots and the membrane or structure, or heat damage to the membrane caused by accidental laser misdirection.

## Slide 100: Risk Management - Results
Technical
Safety
Schedule
Uncertainty about performance in lunar environment
Notes: Finally, we identified a bunch of schedule risk, which were, like the technical risks, mostly caused by uncertainty about some aspects of the system’s performance in the lunar environment.

## Slide 101: Risk Management - Results
Technical
Safety
Schedule
Uncertainty about performance in lunar environment
Mitigated by including margins
Notes: But fortunately, most of these risks are fairly straight forward to mitigate by including margins in the schedules

## Slide 102: Discussion - Considerations
Focus on exploration, not exploitation
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 103: Discussion - Considerations
Focus on exploration, not exploitation
Equally shared benefits
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 104: Discussion - Considerations
Focus on exploration, not exploitation
Equally shared benefits
Shared use through global dialogue
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 105: Discussion - Considerations
Focus on exploration, not exploitation
Equally shared benefits
Shared use through global dialogue
Protect pristine landscape
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 106: Discussion - Considerations
Focus on exploration, not exploitation
Equally shared benefits
Shared use through global dialogue
Protect pristine landscape
ISRU minimizes environmental impact
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 107: Discussion - Considerations
Focus on exploration, not exploitation
Equally shared benefits
Shared use through global dialogue
Protect pristine landscape
ISRU minimizes environmental impact
Design for reuse, robustness & high efficiency
Notes: Beyond all the technical considerations that we had to make, there are also several ethical, societal and environmental considerations that are relevant to our project.
The habitat that we are proposing is generally meant for the early scientific and exploration missions, but these missions are likely going to function as a stepping for future commercial missions. While space agencies will likely put extra care into respectfully interacting with the lunar environment, later commercial missions may not care about that. Therefore it is important to ensure that exploration does not turn into exploitation.
Finally, another large issue is that the new race to the moon is only a contest between the very richest and most advanced of nations, even more so than the current LEO space race, so international frameworks that ensure that the benefits of lunar exploration are shared equally amongst humanity should be considered

## Slide 108: Conclusion
Selective Laser Melting
Notes: Initially, two preliminary concept were developed simultaneously and evaluated
Here, concept 2 came out on top due to its lower technical complexity, higher flexibility and adaptability, quicker construction time and lower cost.

## Slide 109: Conclusion
Selective Laser Melting
Concept Evaluation
Notes: Next, several additive manufacturing methods were investigated; here, selective laser melting was found to be the best option, due to its ability to create strong, geometrically complex shapes without the needs for any additives.

## Slide 110: Conclusion
Selective Laser Melting
Concept evaluation
Catenary dome with infill pattern
Notes: Since it is not possible to use manual labor in the construction process, it was necessary to rely on construction using robotic swarms
For this, requirements were devised for all the robots and supporting systems
Furthermore, several options for the collector/depositor, flattening and melting robots were investigated, by investigating real robotic systems under development that aim to perform the same functions as the ones we are envisioning

## Slide 111: Conclusion
Selective Laser Melting
Concept evaluation
Catenary dome with infill pattern
Robotic swarm construction
Notes: Since it is not possible to use manual labor in the construction process, it was necessary to rely on construction using robotic swarms
For this, requirements were devised for all the robots and supporting systems
Furthermore, several options for the collector/depositor, flattening and melting robots were investigated, by investigating real robotic systems under development that aim to perform the same functions as the ones we are envisioning

## Slide 112: Conclusion
Selective Laser Melting
Concept evaluation
Catenary dome with infill pattern
Robotic swarm construction
Day-time only operations only viable option
Notes: During development of the construction process and analysis of the power requirements, we came to the conclusion that limiting construction if the construction process would be continuous, a staggering 67 tons of batteries would be required, ballooning the total mission cost to roughly 76 billion, in comparison, limiting construction to only during the day, total mission costs can be reduced by over 90% to 7,6 billion

## Slide 113: Limitations & Future Work
Feasibility of large-scale multi-layer SLM
Notes: There are still several big questions and research topics that need to be answered before a real mission aimed at constructing a habitat on the moon can begin.
One of the biggest possible hurdles facing such a project are the questions that remain about the feasibility of large-scale multi-layer SLM in a lunar environment.
Although many experiments have been conducted that successfully melted small samples of lunar regolith together, not many tests have been conducted that try to create multi layer structures using this method.
That’s why many
questions remain about aspects like melting performance under vacuum conditions, layer adhesion and optical particle size range.
One promising solution that was mentioned by one of the experts that we spoke to was to perform multiple passes.

## Slide 114: Limitations & Future Work
Feasibility of large-scale multi-layer SLM
Lunar environment
Notes: Another big area of uncertainty remains the lunar environment and its effects.
One of the biggest risks that we do not really have an answer for is the danger from moon quakes. Much is still unknown about their nature, frequency and maximum magnitudes.
Another such area is the performance of the robotic systems in the actual lunar environment; it is possible that systems behave in unexpected ways once they operate in a real lunar environment, especially the long-term durability and rate of performance degradation of systems remains a question

## Slide 115: Limitations & Future Work
Feasibility of large-scale multi-layer SLM
Lunar environment
Power generation systems
Notes: Finally, future studies could look into the possibility of utilizing other power systems. The big limitation of the solar + battery option is that it would need a prohibitive amount of battery storage capacity, which is the main cost driver in our continuous printing scenario, although we were able to mitigate that by limiting printing to the lunar day, when the habitat will eventually be inhabited by human occupants, it will likely not be an option to limit power consumption that drastically during the lunar night.
Possible alternatives include nuclear power generation or replacing the battery system with a regenerative fuel cell (RFC) system.

## Slide 116
Back to the Moon
Notes: So that was our presentation, we hope that we have demonstrated that, although many challenges still remain, lunar construction is not as infeasible as it may seem at first glance, and we hope that our findings may be of use when humans one day will go back to the moon

## Slide 117
Back to the Moon
By combining swarm robotics and additive manufacturing of lunar regolith we have developed a solution to autonomously construct a protective habitat inside a lava tube to facilitate permanent human presence on the moon.

## Slide 118: Concept Selection: Relative Importance
 | TC | TM&R | A | R&M | SI&D | CT | LC
TC | X | 1 | 5 | 4 | - | 7 | -
TM&R | - | X | 5 | 4 | - | 7 | -
A | - | - | X | - | - | 2 | -
R&M | - | - | 5 | X | 1 | 5 | -
SI&D | 2 | 2 | 6 | - | X | 6 | -
CT- | - | - | - | - | - | X | -
LC | 3 | 3 | 7 | 2 | 2 | 8 | X
-Technical Complexity (TC)
-Technological Maturity and Risk (TM&R)
-Adaptability (A)
-Reliability and Maintenance (R&M)
-Structural Integrity and Durability (SI&D)
-Construction Time (CT)
-Logistical Cost (LC)

## Slide 119: Concept Selection: Score assignment
Criteria | Weight | Rank | Score |  | Weighted Score | 
 |  |  | Blocks | In-Situ | Blocks | In-Situ
TC | 0,169 | 3 | 2 | 2,2 | 0,34 | 0,37
TM&R | 0,169 | 3 | 2,8 | 1,8 | 0,47 | 0,30
A | 0,032 | 6 | 1,6 | 3,4 | 0,05 | 0,11
R&M | 0,107 | 5 | 1,6 | 2,6 | 0,17 | 0,28
SI&D | 0,192 | 2 | 2,8 | 3,2 | 0,54 | 0,61
CT- | 0,024 | 7 | 2,2 | 2,4 | 0,05 | 0,06
LC | 0,306 | 1 | 2,4 | 3 | 0,73 | 0,92
Total |  |  |  |  | 2,36 | 2,95

## Slide 120: Robot characteristics
COLLECTORS |  | 
Weight | 30 | [kg]
Speed | 0,3 | [m/s]
Collecting time | 200 | [s]
Unloading time | 100 | [s]
Mass collected per trip | 30 | [kg]
Charging time | 68 | [m]
Cooling time | 121 | [m]
Operating time | 90 | [m]
Maintenance time | 20 | [%]
FLATTENERS |  | 
Weight | 25 | [kg]
Speed | 0,3 | [m/s]
Flattening speed | 50 | [m2/h]
Charging time | 45 | [m]
Operating time | 180 | [m]
Maintenance time | 4 | [%]
MELTERS |  | 
Weight | 330 | [kg]
Printing speed | 1,725 | [l/h]
Unloading time | 100 | [s]
Maintenance time | 4 | [%]

## Slide 121: Systems characteristics and distances
PROCESSING |  | 
Output Rate | 150 | [kg/h]
Output Buffer | 750 | [kg]
Input Buffer | 750 | [kg]
CHARGING STATIONS |  | 
Weight | 2,9 | [kg]
Charging Power | 470 | [W]
Efficiency | 0,85 | 
DISTANCIES | Excavation site | Structure
Charging stations/ processing machine | 350 [m] | 45 [m]

## Slide 122: Laser Power Calculation
Regolith properties | 
Density (ρ) | 1500 [kg/m3]
Specific heat capacity (Cp) | 1000 [J/K/kg]
Laten heat of fusion (Lf) | 4,6 × 105 [J/kg]
Temperature | 
∆T | 1520 [kg]
Laser | 
Efficiency (η) | 0,5
Printing rate (V) | 0,5 [cm3/s]
Guo, Z.-S., Li, M., Xing, D., Liang, C.-G., Hao, B., & Ma, P.-C. (2025). Melting and solidifying behavior of lunar regolith simulant under a vacuum environment. Journal of the American Ceramic Society, 108(8), e20566. https://doi.org/10.1111/JACE.20566
Evol = ρ∙ Ekg = 2,97 × 109 J/m3
Pideal = Evol ∙V = 1485 W
Pactual = Pideal ∙ η = 2970 W
Ekg = Cp∙∆T + Lf = 1,98 × 106 J/kg

## Slide 123: Detail cost
 | Price per unit [ € ] | Number of units [-] | Total [ € ]
Collector Robot | 800.000 | 12 | 9.600.000
Melting Robot | 2.000.000 | 5 | 10.000.000
Flattening Robot | 500.000 | 5 | 2.500.000
Power system | 465.938,81 | 1 | 465.938,81
Processor | 100.000 | 2 | 200.000
Airlock & Membrane | 100.000.000 | 1 | 100.000.000
Comms system | 20.000.000 | 1 | 20.000.000
Charging station | 10.000 | 8 | 80.000
R&D & Testing | 1.000.000.000 | 1 | 1.000.000.000
Software | 100.000.000 | 1 | 100.000.000
Mission control | 800.000.000 | 1 | 800.000.000
Total |  |  | 2.062.845.938,81

## Slide 124: Detail cost
Shipment | Mass [Kg] | Total [ € ]
Collector Robot | 360 | 360.000.000
Melting Robot | 1700 | 1.700.000.000
Flattening Robot | 125 | 125.000.000
Power system | 1553 | 1.553.000.000
Processor | 200 | 200.000.000
Airlock & Membrane | 1100 | 1.100.000.000
Comms system | 200 | 200.000.000
Total |  | 5.238.000.000

## Slide 125: Energy system
System | Mass [Kg]
Battery | 63305
Thermal Control system | 1933
Panel array | 360
Structure | 124
Battery charge controller | 32
Junction and breaker boc | 17
Wire | 14
Total | 65785
Required Systems and Corresponding Mass for a 28.5 kW Setup
Colozza, A. J. (2020). Small Lunar Base Camp and In Situ Resource Utilization Oxygen Production Facility Power System Comparison. NASA. Retrieved from http://www.sti.nasa.gov

## Slide 126: Risk Management Rating
Rating | Likelihood |  | Severity
1 | Rare | (10-5 - 10-4) | Negligible (minimal impact on project objectives)
2 | Very unlikely | (10-4 - 10-3) | Minor (limited impact with manageable consequences)
3 | Unlikely | (10-3 - 10-2) | Significant (noticeable impact requiring mitigation)
4 | Possible | (10-2 - 10-1) | Major (serious impact affecting key project goals)
5 | Probable | (> 10-1) | Catastrophic (would result in end of mission)

## Slide 127: Risk Management Overview
Technical | 20 |  | Mitigate | 11
 |  |  | Research | 5
 |  |  | Watch | 0
 |  |  | Combination | 4
Safety | 7 |  | Mitigate | 4
 |  |  | Research | 3
 |  |  | Watch | 0
 |  |  | Combination | 0
Schedule | 13 |  | Mitigate | 13
 |  |  | Research | 0
 |  |  | Watch | 0
 |  |  | Combination | 1

## Slide 128: Slide division
Manuel: 1 - 27
Alessandro: 28 - 54
Pieter: 55 - 74
Lorenzo: 75 - 95
Twan: 96 - end